## Slide 1
Automated Meter Reading System with Automatic ROI Detection and Socket-Based Distributed Inference
A Master's Thesis Presentation Following the LBC Matrix Framework
Master in Business Intelligence and Big Data Analytics
Notes: Good morning, everyone. My name is [Your Name], and today I'll present my Master's project in Business Intelligence and Big Data Analytics. We've developed an Automated Meter Reading system that tackles the critical bottleneck of manual Region of Interest detection. Our approach uses a distributed, socket-based architecture. We'll navigate this presentation using the LBC Matrix—Literature, Business Need, and Contribution—to provide a structured view of our research and its practical implications.

## Slide 2
L-AXIS: LITERATURE
The Manual ROI Bottleneck
The Baseline Problem
Current edge solutions like Jomjol AI-on-the-Edge require manual Region of Interest (ROI) selection via a web UI.
Configuration Overhead
Users must manually define digit strip boundaries for every installation, creating a significant setup barrier.
Calibration Fragility
Any physical shift in the camera requires manual recalibration, making the system brittle for real-world use.
[Visual: jomjol roi .png - Manual Web UI Configuration]
Figure 1: Manual ROI configuration in the Jomjol baseline system.
Notes: Starting with the Literature axis, we identified a significant gap in existing edge-based AMR solutions. The current baseline, like the Jomjol AI-on-the-Edge device, requires a human operator to manually select the Region of Interest. This isn't just a setup inconvenience; it's a scalability killer. If a camera shifts even slightly, the entire reading pipeline fails until a human manually recalibrates it. This creates a massive deployment bottleneck for real-world utility installations. So, this manual step prevents transition from hobbyist projects to large-scale industrial applications.

## Slide 3
B-AXIS: BUSINESS NEED
The Scalability Problem
Operational Costs
Manual interventions can't scale to hundreds of thousands of meters.
Autonomy Requirement
Deployments need "install and forget" robustness to environment and camera shifts.
Maintenance Reduction
Removing UI configuration cuts TCO and ongoing maintenance.
The Core Objective
Convert the AMR pipeline into a self-correcting autonomous system that removes manual configuration bottlenecks.
Notes: Moving to the Business Need, the motivation is clear: scalability. Utility companies manage hundreds of thousands of meters. A system that requires even five minutes of manual UI configuration per meter is economically unviable at scale. The business requirement is a fully autonomous pipeline that can handle small camera shifts without intervention. By automating the ROI detection, we move from a high-maintenance hobbyist tool to a robust industrial solution. This significantly reduces operational overhead and enables massive, low-cost deployments. This transforms the AMR pipeline from a supervised setup to a fully autonomous, self-correcting system.

## Slide 4
C-AXIS: CONTRIBUTION
Distributed Architecture
Machine A
Client / Edge
Captures high-resolution meter images.
Runs lightweight YOLOv8n for ROI extraction.
Transmits cropped image bytes via TCP sockets.
—
—
—
Machine B
Server / Inference
Receives and processes incoming image crops.
Performs OpenCV-based digit segmentation.
Executes CNN classification for final reading.
—
—
—
[Visual: Architecture Flowchart]
Client (YOLO) → Socket → Server (CNN)
Figure 2: Distributed acquisition and inference pipeline.
Notes: Our primary Contribution is a distributed architecture that bridges the gap between edge capture and powerful inference. We use a two-machine setup connected via TCP sockets. Machine A, the client, captures images and runs a lightweight YOLOv8n model for real-time ROI extraction. This cropped image is then sent to Machine B, the server. The server handles the more computationally intensive tasks: OpenCV-based segmentation and CNN-based digit classification. This separation of concerns allows for a responsive system that doesn't overtax edge hardware while maintaining high-fidelity inference.

## Slide 5
C-AXIS: CONTRIBUTION
Component Validation
100%
YOLOv8n ROI Success
Perfect detection rate on 50 test images. Performance reached 99.34% mAP@50 and 75.62% mAP@50-95.
[Visual: yolo crop.png - ROI Bounding Box]
99.00%
CNN Classification Accuracy
Trained on 9,960 digit crops. Final hold-out accuracy achieved with a macro average of 0.99.
[Visual: cnn detection.png - "05866" Reading]
Notes: To validate our contribution, we rigorously tested each component. The YOLOv8n model achieved a perfect 100% success rate in detecting the ROI across our test images. It showed a mean Average Precision of 99.34%. For digit classification, we trained a custom CNN on nearly 10,000 samples. The results were exceptional, reaching 99.00% accuracy on the hold-out test set. We used early stopping to ensure the model was well-generalized. These high component-level metrics provide a solid foundation for the end-to-end pipeline. Next, we'll see how this compares to existing solutions.

## Slide 6
STATE OF THE ART
Benchmark Comparison
System
ROI Localization
Autonomy
Scalability
Traditional CV
Fixed / Manual
Low
Low
Legacy Edge (Jomjol)
Manual Web UI
Low
Medium
Laroca et al.
Automatic (Server)
High
Low (Resource Heavy)
Proposed System
Automatic (YOLO)
High
High (Distributed)
Key Positioning: The proposed solution bridges the gap between high-autonomy server models and low-cost edge hardware by combining automatic ROI detection with a distributed socket-based architecture.
Notes: After validating our individual components, we need to understand where our system stands against the state of the art. Our solution carves out a unique niche in the landscape of automated meter reading. We combine fully automatic ROI detection with a distributed edge-server model. This approach bridges the gap between highly autonomous, but resource-heavy, server-side solutions and low-cost, but manually intensive, edge devices. It offers a practical, scalable middle ground for industrial utility deployments. Now, let's look at how this system performs end-to-end.

## Slide 7
EXPERIMENTAL RESULTS
End-to-End Results & Error Analysis
72.00%
Exact Full-Reading Match
Achieved on 50 local test images under varying conditions.
76.00%
Correct Text-Length Prediction
Reflects the system's ability to correctly identify the number of digits present.
[Visual: cnn error.jpg - Segmentation Failure]
Segmentation Bottleneck
The primary limitation is deterministic OpenCV under-segmentation. Glare and reflections can erase visible gaps between digits, causing the system to merge them. Example: A real reading of "21931" was incorrectly reconstructed as "43" due to reflection-induced merging.
Notes: While our components performed exceptionally well, the real-world end-to-end pipeline presents its own challenges. We achieved a 72% exact match rate for full meter readings, and a 76% accuracy in predicting the correct number of digits. The primary limitation isn't the AI classification itself, but rather the deterministic OpenCV segmentation. Glare and reflections can cause digits to merge, leading to incorrect reconstructions. For example, a five-digit reading might be misinterpreted as two digits. This highlights that while we've solved the ROI problem, robust segmentation in varied lighting is the next critical hurdle. This brings us to our conclusions and future work.

## Slide 8
Conclusion & Future Work
KEY ACHIEVEMENTS
Bottleneck Removal
Successfully eliminated manual ROI configuration, enabling fully autonomous deployment for AMR systems.
High-Fidelity Components
Demonstrated 100% ROI detection success and 99.00% digit classification accuracy on hold-out test sets.
Practical Architecture
The distributed socket-based design provides a scalable path for industrial utility monitoring.
FUTURE DIRECTIONS
Robust Segmentation
Moving from deterministic OpenCV methods to deep-learning-based segmentation to handle glare and reflections.
End-to-End OCR
Transitioning toward sequence-based recognition models (e.g., CRNN) to eliminate the need for explicit digit segmentation.
The proposed system bridges the gap between high-autonomy server models and low-cost edge hardware, offering a viable industrial solution.
Notes: In conclusion, this project successfully eliminates the manual ROI bottleneck that has limited the scalability of edge-based AMR systems. We've demonstrated that a distributed architecture, supported by high-performing YOLO and CNN components, provides a viable path toward autonomous utility monitoring. While segmentation remains a challenge in difficult lighting, the foundation is now firmly in place. Future work will focus on moving away from deterministic segmentation toward end-to-end sequence recognition, further increasing the system's robustness in the field. This concludes my formal presentation.

## Slide 9
Questions & Answers
Thank you for your time and attention.
Master in Business Intelligence and Big Data Analytics
Notes: That concludes my presentation. I want to thank you for your time and attention. I am now open to any questions you may have regarding the architecture, the experimental results, or the future directions of this research.